## Slide 1
Notes: 1
Many of these charts have animation and speaker notes.
Version 1.0

## Slide 2
Introduction to Embedded Systems
Version 2.0

## Slide 3
3
Date
Version
Description
Modified By
Reviewed & Approved by
17-Nov-09
1.0
Initial Version
Notes: 3
Version 1.0

## Slide 4
4
What is Embedded System?
What is a Real Time System?
Entities in an Embedded System
Entities in a CPU
Timers
Interrupts
Memory
  Cache.
  MMU
RTOS
Boot-Loader
Kernel
User-space
Kernel-space
Process/Threads
Synchronization Mechanisms IPC
Interrupts
Debugging
Notes: 4
Version 1.0

## Slide 5: What is Embedded System?
Designed to perform one or few dedicated functions.
Consists of CPU, Memory, I/O and External devices, which are needed to accomplish the dedicated functions.
Designed to reduce the size and cost of the product and increase the reliability and performance
Designed based on General / Real-Time OS or even without OS (Microcontrollers)
Examples:
  MP3 Player, Digicam

## Slide 6: What are Real-time Systems ?
Execute within time constraints
Deadline must be met
  Time and Memory
Examples:
  ABS in automobiles
  Aircraft Control Systems
  Pacemakers
6

## Slide 7: Entities in an Embedded System (CPU and Peripherals)
[ Scope:- Mention what are the main entities in a typical embedded system. Below is an example. ]

## Slide 8: CPU Entities
To the trainer:Mention what are the main entities in a typical CPU.

## Slide 9: CPU Entities (Cont.)
Arithmetic logic unit (ALU) is a digital circuit that performs arithmetic and logical operations.
  Most ALU use two’s compliment number system.
Common operations:
  Integer arithmetic operations(Addition & Subtraction).
  Bitwise logical operations (AND, OR,NOT,XOR).
  Bit shifting Operations (multiplications by 2 and divisions by 2)
Address bus (that may be 8, 16 or 32 bits wide) carries address for accessing memory location

## Slide 10: CPU Entities (Cont.)
Data bus (that may be 8, 16 or 32 bits wide) carries data to memory or receive data from memory.
RD (Read) and WR (Write) line to tell the memory whether it wants to set or get the addressed location.
Clock line that lets a clock pulse sequence the processor.
Reset line that resets the program counter to zero (or whatever) and restarts execution.
Registers A, B and C are simply latches made out of flip-flops.
Program counter is a latch with the extra ability to increment by 1 when told to do so, and also to reset to zero.

## Slide 11: Real Time Clock (RTC)
A RTC is a computer clock that keeps track of the current time.
RTCs often have an alternate source of power
  Low power consumption (important when running from alternate power).
  Frees the main system for time-critical tasks.

## Slide 12: TIMERS
A timer is a specialized type of clock. A timer can be used to control the sequence of an event or process.
Computer systems usually have at least one timer. These are typically digital counters that either increment or decrement at a fixed frequency, which is often configurable, and that interrupt the processor when reaching zero.
As the number of hardware timers in a computer system or processor is finite and limited, operating systems and embedded systems often use a single hardware timer to implement an extensible set of software timers.
[ Scope:- Explain hw and sw timers ]

## Slide 13: Watchdog Timer (WDT)
A watchdog timer (WDT) is a device that resets the processor after a certain period of time, if something goes wrong and the system does not recover on its own.

## Slide 14: Memory Types
Volatile
Non-Volatile
SW re-writable
SW non-re-writable

## Slide 15: FLASH - NOR and NAND
Comparison of NOR vs NAND
NAND is generally used for large memory requirement and low cost.
NOR is used in systems which need fast access. NOR chips are costlier than NAND

## Slide 16: RAM (SRAM, DRAM)
DRAM
  Cheaper
  Slower
  Needs continuous clock triggers to refresh charge in the capacitors
SRAM:
  Costlier
  Faster
  Needs no continuous clock triggers (uses flip-flops)

## Slide 17: MMU - Address space
Logical Vs Physical Address space
  Logical address – generated by the CPU; also referred to as virtual address.
  Physical address – address seen by the memory unit.
Usually, Memory Management Unit (MMU) is a hardware device that maps virtual to physical address.
In MMU scheme, the value in the relocation register is added to every address generated by a user process at the time it is sent to memory.

## Slide 18: MMU - Address binding
Address binding of instructions and data to memory addresses can happen at three different stages.
Compile time: If memory location known a priori, absolute code can be generated; must recompile code if starting location changes.
Load time: Must generate relocatable code if memory location is not known at compile time.
Execution time: Binding delayed until run time if the process can be moved during its execution from one memory segment to another. Need hardware support for address maps (e.g., base and limit registers).

## Slide 19: Swapping, Paging, Segmentation
Program must be brought into memory and placed within a process for it to be run.
Swapping of programs to maximize memory utilization
Unavailability of contiguous memory while swapping in a program due to memory fragmentation
Paging - Divide physical memory into fixed-sized blocks called frames and logical memory into blocks of same size called pages.
To run a program of size n pages, need to find n free frames and load program.
Set up a page table to translate logical to physical addresses.
Segmentation - Memory-management scheme that supports user view of memory. Examples include CS, DS, SS, ES, etc.

## Slide 20: 80386 Segmentation + Paging Unit

## Slide 21: Cache
Cache is a short-term storage and it can speed up the operations by temporarily placing data where it can be accessed more rapidly than normal.
iCache – Instruction Cache
dCache – Data Cache

## Slide 22: Cache (Cont.)

## Slide 23: Cache (Cont.)
Cache Hit:
Finding and retrieving an instruction or item of data in a cache.
Cache Miss:
A failure to find the required instruction or data in the cache.
Hit rate or Hit ratio of the cache:
The percentage of access that result in cache hit is known as hit rate or hit ratio of the cache.

## Slide 24: Cache (Cont.) – Write policies
Write-back cache:
Data normally written into the cache first.
During the idle machine cycles, the data are written from the cache into memory or onto disk.
Improves the performance, because a write to the high-speed cache is faster than to normal RAM or disk.
With this performance improvement comes a slight risk that data may be lost if the system crashes.
Write-through cache:
Data written by the CPU to memory or to disk is also written into the cache.
Write performance is not improved but subsequent read operation will be improved, because the data are already in the high-speed cache.

## Slide 25: What is an Operating System?
It is a software, consisting of programs and data, that runs on computers and
manages computer hardware resources.
Types of OS:
  General Purpose OS
  Real-Time OS

## Slide 26: What is a Real Time Operating System?
A real-time operating system (RTOS) is an operating system (OS) intended to serve real-time application needs.
Real-time operating systems have " deterministic " timing behavior.
A real-time OS has an advanced algorithm for scheduling.
Real-time OS have minimal interrupt latency and minimal thread switching latency

## Slide 27: RTOS - Scheduling
Scheduling refers to the way processes are assigned to run on the available CPUs, since there are typically many more processes running than there are available CPUs. This assignment is carried out by software known as a scheduler and dispatcher.
Some scheduling algorithms include,
  Cooperative scheduling
  Preemptive scheduling
    Rate-monotonic scheduling
    Round-robin scheduling
  Earliest Deadline First approach

## Slide 28: RTOS - Types
Hard real-time or immediate real-time system:
Missing deadline may cause a critical failure of the system (Pacemaker – creating pulses within hard time limit)
Soft real-time system:
Tolerates lateness beyond deadline and may respond with decreased service quality (e.g., omitting frames while displaying a video).

## Slide 29: What is Boot-loader?
Software that initializes the minimal required peripherals during boot.
  Example: Clocks, CPU control registers, Memory
Load and kick start the OS.
  OS requires some registers to be loaded with values such as entry points etc.
  Responsible for initializing other peripherals like Ethernet, USB, SD-Card.

## Slide 30: What is a Kernel?
[ Scope:- Introduce the Kernel and user space. Also talk about protected mode ]
  Kernel can be thought of as the program which controls all other programs on the computer. Its responsibilities include managing the system's resources such as hardware and memory.
  Virtual memory allows multiple programs to load in memory at the same time. Each application addresses memory starting at zero, but virtual memory takes control of the memory addressing and lets each application function as if it had unlimited memory.

## Slide 31: Kernel Space
Kernel space is a privileged area; the user has access to it only through the system call interface
Kernel process can modify the memory map, an operation frequently required to perform process scheduling
A user process runs in kernel context when it executes a system call and executes kernel code

## Slide 32: User Space
User space is the area in memory where user processes are run
A process executing in user space is said to be operating in user mode

## Slide 33: User & Kernel Space Layout

## Slide 34: Process and Thread – A comparison
Process
A process is an executing instance of an application
Processes have their own address space
Threads can directly communicate with other threads of its process
Heavy context switching
Thread
A thread is a path of execution within a process
Threads within the same process share the same address space
Processes must use IPC to communicate with sibling processes
Light weight context switching

## Slide 35: Types of Process
Parent Process
  Process 1 is parent of all the process, Any process if creates a new process than it becomes a parent process to the newly created process
Child Process
  All the process except Process 0 are child processes.
Orphan process
  When Parent dies before child exits
  Child process is adopted by init , i.e. its parent becomes init i.e. process id 1
  Init does a wait on the orphaned child process , handles cleanup from process table on exit
Defunct or zombie process
  child process exits, but still has an entry in the process table
  parent is notified with a SIGCHLD
  The child is in “defunct or zombie” state till the parent does a “wait” and reads the exit status of the child
  Child process does not consume CPU resources, only sits in the Process table

## Slide 36: Process memory structure
text
initialized Data
uninitialized Data
heap
stack
sp (Stack Pointer)
pc (Program Counter)
fd0
fd1
fd2
fd3
fd table
High Address
Process Memory
Process Control Block
Each Process has its own
  Program Counter
  Stack
  Stack Pointer
  Address Space
Process May Share
  Data
  Code
Low Address

## Slide 37: Some Process Control functions
Below listed are few important functions for process
Create process
  fork()
  Vfork()
  Exec ()
Exit process
  exit()
  return()
  abort()
Wait for child status
  wait()
  waitpid()
Dynamic Priority changing
  nice()
  getpriority()
  setpriority()
  renice()
Note: To know more details please refer manual page in Linux with command man <function name>

## Slide 38: Example of a Process
  #include <stdio.h>
  int main( ) {
    int pid, status;
    pid = fork();
    if( pid == 0 ) {
    printf(“inside child\n”); /* Here we can run different functions,
    sleep(2);
    exit(0); /* exiting from child*/
    } else {
    printf(“Inside parent\n”);
    if( wait( &status ) == pid )
    printf( “Child exited\n” );
    }
    exit(0); /* Exiting from parent */
  }

## Slide 39: Thread Memory Structure
text
Initialized data
Uninitialized data
heap
stack2
stack3
sp1 (Stack Pointer)
pc1 (Program Counter)
fd0
fd1
fd2
fd3
fd table
High Address
Process Memory
Process Control Block
stack1
sp2 (Stack Pointer)
pc2 (Program Counter)
sp3 (Stack Pointer)
pc3 (Program Counter)
Lower Address
Each thread has its own
  Program Counter
  Stack
  Stack Pointer
Threads May Share
  Address space
    Code
  Open files

## Slide 40: Thread usage Example
  #include <stdio.h>
  #include <stdlib.h>
  #include <pthread.h>
  #define FAILURE -1
  #define SUCCESS 0
  void* DisplayMessage(void* msg) {
  int status = 0;
  printf("I am in the thread.. %s\n", (char*)msg);
  pthread_exit(&status);
  }
  int main() {
  char* msg1 = "Thread1";
  char* msg2 = "Thread2";
  pthread_t thread1, thread2;
  int ret = 0;
  ret = pthread_create(&thread1, NULL, DisplayMessage, (void*) msg1);
  if (ret != 0) {
  fprintf(stderr,"Error occured while creating thread1..\n");
  exit(FAILURE);
  }
  ret = pthread_create(&thread2, NULL, DisplayMessage, (void*) msg2);
  if (ret != 0) {
  fprintf(stderr,"Error occured while creating thread2..\n");
  exit(FAILURE);
  }
  printf("I am in main thread...\n");
  exit(SUCCESS);
  }

## Slide 41: Task synchronization
Task synchronization can be achieved by using below two ways,
  Semaphore
  Mutex

## Slide 42: Semaphore (1)
A semaphore is a protected variable or abstract data type that provides a simple but useful abstraction for controlling access by multiple processes to a common resource in a parallel programming environment.
Synchronize multiple tasks for a critical resource access
Two variants
  Counting semaphore
  Binary semaphore.
A semaphore is created with initial_count, which is the number of allowed holders of the semaphore lock. (initial_count=1: binary sem)
A task can get the semaphore when the count > 0; otherwise, block on it.

## Slide 43: Semaphore (2)
  Two operations:
  P(S): get or wait for semaphore
  V(S): release semaphore
Disadvantages (problems) with semaphores
  Deadlocks
  Loss of mutual exclusion
  Blocking tasks with higher priorities (e.g. FIFO)
  Priority inversion

## Slide 44: Priority Inversion (1)
Priority inversion problem
  Assume 3 tasks: A, B, C with priorities Ap<Bp<Cp
  Assume semaphore: S shared by A and C
  The following may happen:
    A gets S by P(S)
    C wants S by P(S) and blocked
    B is released and preempts A
    Now B can run for a long long period .....
    A is blocked by B, and C is blocked by A
    So C is blocked by B
It can be much worse if there are more tasks with priorities in between Bp and Cp, that may block C as B does.

## Slide 45: Priority Inversion - Demo

## Slide 46: Priority Inversion (2)
Solution?
  Task A with low priority holds S that task C with highest priority is waiting.
  Task A can not be forced to give up S, but A can be
preempted by B because B has higher priority and can run without S.
So the problem is that ’A can be preempted by B’
  High A’s priority when it gets a semaphore shared with a task with higher priority! So that A can run until it release S and then gets back its own priority

## Slide 47: MUTual EXclusion
[ To be done: Simplify ]
Special kind of semaphore for providing mutual exclusion.
Provides ‘Lock’ and ‘Unlock’ services.
Task which locks a Mutex becomes its owner.
Other tasks trying to lock will be blocked.
Only the owner can unlock a Mutex.
If another task is blocked waiting for this Mutex, Its becomes its owner.
Mutex don’t have a count.
Mutex can solve Unbounded priority inversion.

## Slide 48: Inter-Process Communication
Exchange of data between two or more, separate independent processes/threads.
Operating systems provide facilities/resources for inter-process communications (IPC), such as,
  FIFO,
  Message queues,
  Shared memory,
  Signals

## Slide 49: Message Queue API & Description
What is Message Queue?
A message queue provides a buffered communication method for tasks.
Message queues also provide a way to communicate without copying data, which can save time.
Logically two queues are maintained in the message queue:
  One for message buffers which are currently not being used (known as the “free” queue).
  The other holds messages which have been sent but not yet received (known as the “send” queue). (Add Diagram)

## Slide 50: Shared memory
Shared memory provides an efficient way of sharing data between multiple processes. It allows two unrelated processes to access the same logical memory.
Shared memory is a special range of addresses that is created by IPC for one process and appears in the address space of that process. Other processes can then 'attach' the same shared memory segment into their own address space.
Programmer has to take care of synchronized access.

## Slide 51: Signals
A signal is an event generated by the system in response to some condition, upon receipt of which a process may in turn take some action.
They are generated by the shell and terminal handlers to cause interrupts. They can also be explicitly sent from one process to another as a way of passing information or modifying behavior.
Example
If typing the interrupt character (often Ctrl−C) at the keyboard will result in the SIGINT signal being sent to the foreground process, i.e. the program currently running. This will cause the program to terminate unless it has arranged to catch the signal.

## Slide 52
Interrupt is an asynchronous signal indicating the need for processor attention.
Example: Keyboard generates an interrupt to read key pressed.
Types of Interrupts.
  – Reset (Highest Priority)
  – Software Interrupts and Exceptions
  – Non-Maskable Interrupts (NMI): From External Hardware
  – Maskable Interrupts (Lowest Priority)
Interrupt latency is the time between the generation of an interrupt by a device and the servicing of the device which generated the interrupt.
Interrupts
52

## Slide 53: Interrupt service routine (ISR)
ISR is a callback subroutine which is executed by the reception of an interrupt.
  Save IRQ (Interrupt Request) value and the registers to the kernel mode stack.
  Send ack to the CPU/Programmable Interrupt Controller (PIC) thus allowing it to issue next interrupt.
  Execute ISRs associated with all the devices that share same IRQ.
  Execute active softirqs.
  Terminate by jumping.

## Slide 54
Hardware Interrupts are generated from an external device, connected to processor through interrupt controller.
  Maskable interrupt may be ignored by setting a bit in an interrupt mask register(IMR) bit-mask. Ex: Keyboard, Mouse
  Non-maskable interrupt (NMI) lacks an associated bit-mask, so that it can never be ignored. Ex: Watch dog Timers,
Software interrupt is an interrupt generated within a processor by executing an instruction.
Ex: Signals like sig_term sent to terminate a process.
Exceptions, which are used to report grave runtime errors. Interrupts such as the int 0x80 instruction used to implement system calls on the x86 architecture
Hardware & Software Interrupts
54

## Slide 55: Do’s & Don'ts in ISR
Interrupt handlers should not relinquish the processor by calling sleepy functions.
Mutexes should not be used for protecting critical sections inside interrupt handlers instead use spinlock.
Interrupt handlers cannot directly exchange data with user space (Discussed later)
Design interrupt handlers to be reentrant.

## Slide 56: Common Debugging Techniques
Writing code to support debugging
    Using Asserts
    Magic debug values
    Debugging by Printing/software tracing/log file
Debugging is tightly coupled to the system development environment.
OS provides certain utilities for debugging.

## Slide 57: Common Debugging Techniques (Cont.)
Debugging by Querying
    By querying the process. eg: using proc file system on linux
Debugging by Watching
    Sometimes minor problems can be tracked down by watching the behavior of an application in user space eg: strace on Unix platforms
Debuggers
    Eg GDB, trace32, GreenHills probe

## Slide 58: Debuggers-Advantages
Advantages:
Source level debugging
Step and trace
Change program execution state.
Conditional breakpoints
Watches
Call stack

## Slide 59: ICE (In circuit emulator)
An in-circuit emulator (ICE) is a hardware device used to debug the software of an embedded system.
The programmer uses the emulator to load programs into the embedded system, run them, step through them slowly, and view and change data used by the system's software.
An "emulator" gets its name because it emulates (imitates) the central processing unit of the embedded system's computer. Traditionally it had a plug that inserts into the socket where the CPU chip would normally be placed. Most modern systems use the target system's CPU directly, with special JTAG-based debug access.

## Slide 60: ICE - JTAG
JTAG or Joint Test Action Group is a method of accessing memory and CPU resources without having an application running on the target.
BDM or background debugging mode also achieves this objective.
JTAG is standardized as IEEE 1149.1 Standard Test Access Port and Boundary-Scan Architecture.
JTAG aware hardware devices can be debugged using JTAG supported debuggers. Eg: Lauterbach Trace32 ICD and green hills (super probe) and Time machine suite

## Slide 61: ICE - Notes
Recent ICEs enable a programmer to access the on-chip debug circuit that is integrated into the CPU via JTAG or BDM (Background Debug Mode) in order to debug the software of an embedded system. These systems often use a standard version of the CPU chip, and can simply attach to a debug port on a production system.
They are sometimes called in-circuit debuggers or ICDs, to distinguish the fact that they do not replicate the functionality of the CPU, but instead control an already existing, standard CPU.
OS aware debuggers may be needed to help in debugging systems with Virtual memory

## Slide 62: Kernel Debugger
A kernel debugger is a debugger present in some kernels to ease debugging and kernel development by the kernel developers.
A kernel debugger might be a stub implementing low-level operations, with a full-blown debugger such as gdb, running on another machine, sending commands to the stub over a serial line or a network connection, or it might provide a command line that can be used directly on the machine being debugged.
Examples:
  Windows : KD, rasta ring 0, softice
  Linux : KDB

## Slide 63: Memory debugger
Memory corruptions give rise to strange, bizarre and program crash.
To ease debugging of memory, memory debuggers are used.
Memory debuggers work by monitoring memory access, allocations, and de-allocation of memory.
Example:
  Linux: Valgrind, Electric fence
  Others: rational purify
  DTV: memcheck, mudflap, leaktracer.

## Slide 64
64
Thank you
www.hcltech.com
Notes: 64
Version 1.0